## Slide 1: AUTOMATED WATERING SYSTEM AND PET cat FEED dispatcher
CSE 316: PROJECT
JIHAD (2105011), MAHI (2105013) AND saif (2105030)

## Slide 2: Project Objectives and Goals
Main Objective: To develop a smart, automated home system using the ATmega32 microcontroller that takes care of plant watering and pet care (hydration + feeding), and prevents it from exiting the house, all with minimal human intervention.

## Slide 3: SPECIFIC GOAL-1: 🌱 Automated Plant Watering
Measure soil moisture in real-time.
Use a pump to water the plant when moisture drops below a defined threshold.
Ensure efficient water usage and prevent overwatering

## Slide 4: SPECIFIC GOAL-2: 🐱 Smart Cat Water Drinker
Monitor water level using a water level sensor.
If the water level is low, activate a pump to provide water.
When it reaches a certain level, the sensor will detect it and the pump will cease pumping
Ensure your cat stays hydrated with clean water available 24/7.

## Slide 5: SPECIFIC GOAL-3: 🍽 AUTOMATED CAT FEEDER
Operate a servo motor using a Bluetooth module (HC-05)
Use a 3D printed food dispenser to drop a fixed amount of food by rotating that servo motor.
Ensure your feline friend never misses a meal—even if you do!

## Slide 6: SPECIFIC GOAL-4: prevent cat from exiting 🏃‍
An LDR sensor can be used to detect light coming from a laser beam.
If the cat tries to flee the house (🙀), the light coming from the laser to the sensor will be blocked when the cat passes the laser beam.
If light is blocked then the LDR sensor will trigger a servo motor to close the doors/windows.
Catto stays home 🏡

## Slide 7: Integration and Control
Coordinate all the components through the ATmega32.
Maintain reliability, efficiency, and timing of all subsystems.

## Slide 8: SMART AND SCALABLE DESIGN
Build a modular system that can be improved later
Keep the design cost-effective and easy to replicate

## Slide 9: COMPONENTS TO BE USED
ATmega32 microcontroller
Sensors – soil moisture sensor (capacitive or resistive), water level sensor (e.g. float switch or ultrasonic module HC-SR04), LDR sensor
12 V DC Water– for refilling water bowl
DC servo motor – for food dispenser
DC servo motor – for closing the doors and windows
Timing logic
HC-05 Bluetooth module
3D printed parts, etc

## Slide 13: Soil moisture sensor

## Slide 14: WATERING PLANTS FLOW DIAGRAM
Soil moisture drops
Waits fixed time
Closes value
Sensor detects it
ATMega32 opens valve

## Slide 15: How the Soil Moisture Sensor Works
It has two probes that go into the soil.
It works like this: Wet soil = good conductor ⚡ | Dry soil = poor conductor 🚫
The sensor outputs a voltage level that changes based on moisture content.
The ATmega32 reads this analog signal through its ADC (Analog-to-Digital Converter) pin.
If the moisture is below a threshold, it triggers the valve to open and water the plant.

## Slide 16: FEEDING WATER TO PET CAT
Water level low
Empties old water and opens refill valve
Fills to tequired level, then, Closes value
Sensor detects it
ATMega32 turns pump on

## Slide 17: Cat Water Drinker — Sensor + Pump Operation
When water level falls below a certain point, water level sensor sends a digital/analog signal to ATmega32.
First, the pump activates to suck out any stale/old water.
Then, a clean water valve is opened.
The system monitors until the water level reaches the desired height.
Valve closes. Done. Water is fresh and topped off

## Slide 18: CAT FEED DISPATCHER
Timer reaches a fixed limit (such as 6 hours)
Rotates dispenser
Drops cat food
ATmega32 activates motor

## Slide 19: Food Dispatcher (Rotary Motor + 3D Printed Mechanism)
Motor runs every 6 hours for a specific duration (controlled by ATmega32 timer).
It rotates a portion of the container, releasing a set amount of dry food.
A circular or paddle-wheel style container is 3D printed.
As it turns, one “pocket” of food aligns with the opening and drops food.
After one cycle, it stops.

## Slide 20: Preventing pet cat from exiting the house (LDR sensor + servo motor)
LDR sensor + servo motor: It detects light coming from a laser beam.
If light is blocked (by a passing pet cat) then the LDR sensor will trigger a servo motor to close the doors/windows.
The windows can be opened again using a Bluetooth module (HC-05)

## Slide 21: THANK YOU